## Slide 1: Data Collection Session Guide
Driver Monitoring System
University of St. Thomas
Khongmeng Kormoua

## Slide 2
Before the session
Confirm the rig is ready:
- Camera mounted and aimed at the driver seat.
- Driver's face fully in frame at typical posture.
- Jetson powered and the display connected (Jetson is connected to the right monitor).
- PC powered, monitor on, wheel + pedals should be connected.
[ SCREENSHOT PLACEHOLDER ]
Hardware setup overview photo (e.g., Hardware_setup_v1.jpg from docs/manual/pics).
1

## Slide 3
Power up the Jetson
On the Jetson:
1. Connect power wire to jetson. Wait for the desktop.
2. Open a terminal (Files > right click > Open Terminal, or Ctrl+Alt+T).
If the camera is not detected later, the IMX477 jetson-io setting may have reset after an L4T update. Fix:
sudo /opt/nvidia/jetson-io/jetson-io.py
[ SCREENSHOT PLACEHOLDER ]
Jetson Linux desktop with a terminal window open.
2

## Slide 4
Launch the recorder
In the terminal:
cd ~/Meng/driver-attn-monitor
./tools/start_recording.sh
The launcher activates the dms-infer conda env and opens the DMS Recorder window.
If dms-infer is missing, it falls back to the mp env. You should see one of:
[launcher] activated env: dms-infer
[launcher] activated env: mp (legacy fallback)
[ SCREENSHOT PLACEHOLDER ]
Terminal showing: [launcher] activated env: dms-infer
3

## Slide 5
The DMS Recorder window
The window has two panels:
- LEFT: live camera preview. A red dot appears here while recording.
- RIGHT: status panel + buttons.
Do NOT click Start yet. Wait for the simulator to be ready (next steps).
[ SCREENSHOT PLACEHOLDER ]
DMS Recorder window with numbered callouts pointing to:
1) Live preview
2) Status (IDLE / REC)
3) Elapsed time
4) Recording-to file
5) Last saved file
6) Start / Stop Recording button
7) Quit button
4

## Slide 6
Launch Assetto Corsa on the PC
On the PC:
1. Power on (if not already) and log in.
2. Launch Assetto Corsa via (TODO: Steam / desktop shortcut).
[ SCREENSHOT PLACEHOLDER ]
Assetto Corsa main menu.
5

## Slide 7
Configure the AC session
Lock these in and use the SAME values every session. Consistency matters for labeling.
- Mode: (TODO)
- Track: (TODO)
- Layout: (TODO)
- Car: (TODO)
- Time of day: (TODO)
- Weather: (TODO)
- AI: (TODO)
- Assists: (TODO)
Load into the car. Pause on the grid; do not drive yet.
[ SCREENSHOT PLACEHOLDER ]
Assetto Corsa session configuration screen with the chosen settings.
6

## Slide 8
Start the recording
1. Driver gets into position at the wheel.
2. On the Jetson recorder, click Start Recording.
- Status flips to REC (red)
- Elapsed counter starts at 00:00
- File rec_<timestamp>.mp4 appears under 'Recording to'
- Terminal prints: [REC] start -> recordings/rec_...
3. On the PC: unpause AC and start driving.
[ SCREENSHOT PLACEHOLDER ]
Recorder showing red dot on preview + Status: REC + counter ticking + filename under 'Recording to'.
7

## Slide 9
During the session
Driver runs the planned scenario:
(TODO: laps / events / distractions / drowsiness prompts).
Periodically check the recorder from a non-distracting angle:
- Status must still read REC (red)
- Timer must still be counting
If the status ever shows IDLE mid-session, recording has stopped. Note the time and decide whether to restart.
[ SCREENSHOT PLACEHOLDER ]
Side-by-side: AC gameplay + the Jetson recorder still showing REC + ticking timer.
8

## Slide 10
End the session
1. On the recorder, click Stop Recording.
- Status returns to IDLE
- Filename moves down to 'Last saved'
- Terminal prints: [REC] stop -> recordings/rec_...
2. Click Quit (or close the window).
3. On the PC: stop / exit Assetto Corsa.
[ SCREENSHOT PLACEHOLDER ]
Recorder window with Stop just clicked. Status back to IDLE, filename under 'Last saved'.
9

## Slide 11
After the session
1. Verify the recording plays end-to-end (double-click the .mp4).
2. Log metadata for the session:
(TODO: spreadsheet / sidecar JSON / lab notebook).
Suggested fields: date, participant ID, track, car, settings, scenario, anomalies.
3. Back up the file to:
(TODO: external drive / lab NAS / cloud).
recordings/ is gitignored. Files stay local to the Jetson until backed up.
[ SCREENSHOT PLACEHOLDER ]
File manager view of /recordings/ showing the new rec_YYYYMMDD_HHMMSS.mp4.
10

## Slide 12
Troubleshooting
- Recorder window does not open: launch from a terminal so the error is visible. Pause-on-exit is built into start_recording.sh; read the message before closing.
- Camera not detected: rerun sudo /opt/nvidia/jetson-io/jetson-io.py, select IMX477, reboot.
- ModuleNotFoundError: PIL -> pip install pillow inside the dms-infer env.
- Dropped frames at 720p30 -> swap CPU mp4v writer for GStreamer + nvv4l2h264enc.
- All camera params (resolution, fps, sensor id, flip) live in config.yaml. Edit there, not in tools/record.py.
[ SCREENSHOT PLACEHOLDER ]
Optional: screenshot of a relevant error message (camera failure, PIL ModuleNotFoundError, etc.).
11